## Slide 1: vDPA for Vhost Acceleration
Xiao Wang, Intel

## Slide 2: Agenda
Vhost Evolution
An Ideal Vhost HW ACC Model
vDPA Design and Impl
  DPDK Vhost Lib and vDPA Driver
  QEMU Vhost User Extention
  Upstreaming Status
Acc Vhost with vDPA
Key Takeaways

## Slide 3: Vhost Evolution
Virtio drv
VM0
NIC w/ Switch
Virtio drv
VM1
Pass-thru for virtio?
virtio 0.95&1.0 
Multi-vendor 
LM with Pass-thru 
Stock VM 
HW accelerator comes
QEMU virtio backend
Virtio drv
VM
Kernel vhost
Virtio drv
VM
DPDK vhost
Virtio drv
VM
Vhost in pure SW
Para-V Flexibility 
Virtio dev
Tap
Tap
Virtio dev
Virtio dev
Virtio 0.95
VM0
NIC w/ Switch
Virtio 1.0
VM1
GOAL
SW vhost
Virtio drv
VM
Live Migration
An ideal framework would achieve:
Virtio spec compliant
Pass-thru like perf
Cloud friendly
Multi-vendor

## Slide 4: vDPA: enable data path pass-thru within Para-V
vDPA: vhost Data Path Acceleration
  Build pass-thru like data path within Para-V
  Inherit all PV advantages
Decomposed Data Path on ACC
  DMA Enq/Deq VRING via IOMMU
  Interrupt Notification
    VFIO INTR eventfd associate with IRQFD
    IRQFD as token for irq_bypass Prod/Cons
    Leverage existing posted-interrupt support
  Doorbell Kick
    Add guest physical memory slot for doorbell direct mapping (virito 1.0, MMIO)
    SW Relay IOEVENTFD to trigger doorbell (virtio 0.95, PIO)
ACC = Accelerator (VRING Capable)

## Slide 5: vDPA Design & Impl
Leverage vhost user
  Unified interface for SW/HW
  SW data path fallback
DPDK vhost lib
  vDPA resource management
  API for vDPA register/unregister
  API for device attach/detach to socket
  vdpa_ops: vhost message driven callback
vhost
…
vdpa drv
socket
…
{dev_addr,vdpa_ops}
QEMU
vdpa dev
IOMMU
init
register
Feature
Ring
VFIO

## Slide 6: Partial Pass-thru for Direct Kick
Extend vhost protocol:
VHOST_USER_PROTOCOL_F_HOST_NOTIFIER
Per-queue notify info
Partial Pass-thru: Notify Reg => HW doorbell
No VMEXIT  (virtio1.0)
QEMU
Slave Handler
vhost user
vDPA driver
vDPA device
Virtio Dev
VM
Notify Reg
Notify Reg
Doorbell
Doorbell
Extended Page Table
Slave Channel
Master Channel

## Slide 7: Relay for Virtio 0.95
0.95 kick with PIO
Version aware by negotiated feature
Relay based on ioeventfd
Notify_suppress to reduce VMEXIT

## Slide 8: Acc Vhost with vDPA
HW focus only on data path
On-demand resource assignment
  Offload features
  MQ
Live migrate stock VM to vDPA
  No feature gap
  Cross-backend LM
  Vice Versa

## Slide 9: Upstreaming Status
18’Q2 QEMU vhost user support for vDPA [Merged]
DPDK 18.05 vDPA framework in vhost [Merged]
DPDK 18.05 IFCVF vDPA driver [Merged]
2018 Q3/Q4 support vIOMMU and Posted Interrupt [WIP]
Kernel vDPA (https://lwn.net/Articles/750770/) [RFC]
Para-virtualized device w/ HW acceleration is getting mature.
Welcome on board!

## Slide 10: Credits (in alphabetical order)
Authors:
Cunming Liang
Tiwei Bie
Xiao Wang
Zhihong Wang
Acknowledgements:
Amnon Ilan
Dan Daly
Ferruh Yigit
Jason Wang
Martin Roberts
Maxime Coquelin
Michael S. Tsirkin

## Slide 11: Key Takeaways
vDPA enables vHost HW acceleration in a cloud friendly way
Framework ready for production
Allow multi-vendor HW design

## Slide 12
Thanks!