## Slide 1: Hardware-Level Performance Analysis of Platform I/O
Patrick Lu, Roman Sudarikov
intel

## Slide 2: Legal Disclaimer & Optimization Notice
Optimization Notice
Intel’s compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice. Notice revision #20110804
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit www.intel.com/benchmarks.
INFORMATION IN THIS DOCUMENT IS PROVIDED “AS IS”. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. INTEL ASSUMES NO LIABILITY WHATSOEVER AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO THIS INFORMATION INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
Copyright © 2018, Intel Corporation. All rights reserved. Intel, Pentium, Xeon, Xeon Phi, Core, VTune, Cilk, and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.

## Slide 3: New Modular PCIe Controller Interconnect
Intel® Xeon® Processor E7 v3 Family – 18C Block Diagram
Intel® Xeon® Processor Scalable Family – 28C Block diagram
Prior to Intel® Xeon® Scalable Processor, all PCIe lanes aggregated to single ring stop. In Intel® Xeon® Scalable Processor, 3x16 PCIe lanes split to three mesh stop. (higher concurrent I/O)

## Slide 4: Re-Architected L2 & L3 Cache Hierarchy
Shared L3
2.5MB/core
(inclusive)
Core
L2 (256KB private)
Core
L2 (256KB private)
Core
L2 (256KB private)
Shared L3
1.375MB/core
(non-inclusive)
Core
L2 (1MB private)
Core
L2 (1MB private)
Core
L2 (1MB private)
Previous Architectures
Skylake-SP Architecture
    Shared L3 changed from inclusive to non-inclusive:
        Inclusive (prior architectures)  L3 has copies of all lines in L2
        Non-inclusive (Skylake architecture)  lines in L2 may not exist in L3
On-chip cache balance shifted from shared-distributed
(prior architectures) to private-local (Skylake architecture)
    Shared-distributed  shared-distributed L3 is primary cache
    Private-local  private L2 becomes primary cache with shared L3 used as overflow cache

## Slide 5: Inclusive vs Non-Inclusive L3
    Memory reads fill directly to the L2, no longer to both the L2 and L3
    When a L2 line needs to be removed, both modified and unmodified lines are written back to DRAM
    Data shared across cores are copied into the L3 for servicing future L2 misses
Though software should be agnostic to the change,
it may see different traffic pattern versus prior server implementations
Inclusive L3
(prior architectures)
L2 256kB
2.5 MB
L3
1
2
Memory
Non-Inclusive L3
(Skylake-SP architecture)
L2 1MB
1.375 MB
L3
1
2
Memory
3
3

## Slide 6: Cache Usage on I/O and Core Interactions
Any performance enhancement technology
built around last level cache may need to be revisited
    I/O reads to memory are non-allocating, i.e., if line is not present in LLC it is not allocated; if line is in LLC, it stays there, if it is in one of L2s, it moves or gets copied to LLC
    I/O writes to memory can be allocating or non-allocating based on no-snoop attribute
    Allocating writes: Writes invalidate core caches and allocate the line in LLC cache where I/O is done
    Non-allocating writes: Writes invalidate core caches and update memory
    CPU supports DDIO where a subset of ways (default is 2) in LLC cache is used to allocate data brought in by I/O agents
    DDIO ways can be written by cores, whereas I/O can’t write into core ways

## Slide 7: IIO transaction flow – Overview
IIO – Integrated I/O Controller
  Controls I/O flow between PCIe devices and Main Memory
  “Allocating write transactions”
    PCI Root Port will utilize write buffers backed by LLC core cache when the target write buffer has WB attribute
    Data buffers naturally aged out of cache to main memory
  “Non-Allocating write transactions”
    PCI Root Port Write transactions utilize buffers not backed by cache – write data moves to the iMC without cache delay
DDIO – Data Direct I/O
  Allows Bus Mastering PCI & RDMA I/O to move data directly in/out of LLC Core Caches
  Allocating Write transactions will utilize DDIO
Configurable globally per platform, per Root PCI Port, or per PCI Transaction

## Slide 8: Configuring IIO transaction flow
Option | Disable_all_allocating_flows (PER PLATFORM) | NoSnoopOpWrEn (PER ROOT PORT) | UseAllocatingFlowWr (PER ROOT PORT) | TLP NS Bit (PER PCI IO) | Resulting IIO Write | DDIO | Notes
1 | 1 | X | X | X | Non- Allocating | NO | OPTIONAL PLATFORM GLOBAL
2 | 0 | 0 | 0 | X | Non- Allocating | NO | OPTIONAL PER ROOT PORT
2 | 0 | 0 | 1 | X | Allocating | YES | DEFAULT SETTING PER ROOT PORT
3 | 0 | 1 | X | 0 | Allocating | YES | Enable Per Root and OPTIONAL PER PCI TRANSACTION
3 | 0 | 1 | X | 1 | Non- Allocating | NO | 
    Disable_all_allocating_flows setting trumps all other settings
    when NoSnoopOpWrEn is set to 1, UseAllocatingFlowWr is a don’t care
    when NoSnoopOpWrEn is set to 0, the NS PCI Header bit is a don’t care
Starting with Skylake Server IIO HW will look at the Non-Snoop bit
in the PCI Header to determine allocating or non-allocating flows

## Slide 9: Chassis Performance Monitoring
https://software.intel.com/en-us/blogs/2014/07/11/documentation-for-uncore-performance-monitoring-units
    Core PerfMon can tell SW how it is performing on an iA core - e.g. was the code scheduled to execute efficiently? Were the tasks well balanced?
    Uncore monitoring can give SW a better sense where all that traffic was routed and what was involved in processing it.

## Slide 10: DPDK packet processing using Direct Data I/O
    Core writes RXd preparing for receiving packet
    NIC reads RXd to get buffer address
    NIC writes packet
    NIC writes RXd
    Core reads RXd (polling)
    Core reads packet and performs some action
Most of software thread work in CPU core and local cache
with minimal memory traffic per packet
CPU Socket
CPU Cores
MEMORY CONTROLLER
RAM
1
LLC
Packet
1
5
2
RXd
NIC
4
3
6

## Slide 11: Telemetry points
Intel tools enable performance visibility of the platform at all layers:
hardware with all its key components and software acceleration engines
CPU Socket
CPU Cores
MEMORY CONTROLLER
RAM
1
LLC
Packet
1
5
2
RXd
NIC
4
6
3
Core communicates
with NIC through
PCIe MMIO transactions
Intel DDIO makes LLC the primary target of
DMA operations
Core I/O data
processing
Memory
bandwidth
Writing back descriptors
may result in partial
PCIe transaction
Integration with DPDK

## Slide 12: Understanding PCIe performance
Network Rx
(ItoM/RFO)
Inbound PCIe write
Network Tx
(PCIeRdCur)
MMIO Read
(PRd)
MMIO Write
(WiL)
Inbound PCIe read
Outbound CPU read
Outbound CPU write
Avoid DDIO miss
Avoid writing back
“partial” descriptors
Match workload I/O throughput
Avoid MMIO Rd
Optimize batch size
Look for MMIO
write traffic

## Slide 13: Measuring memory bandwidth
CPU Socket
CPU Cores
MEMORY CONTROLLER
RAM
1
LLC
Packet
1
5
2
RXd
NIC
4
3
6
Reason with memory traffic:
Wrong NUMA allocation
DDIO Miss
CPU data structure
No memory traffic: Best
Fix it in the code!
Receive packets ASAP, descriptor ring sizes (needs tuning)
May be okay, but check for latency!

## Slide 14: Measuring cross socket bandwidth
CPU Socket
CPU Cores
UPI CONTROLLER
1
LLC
Packet
RXd
NIC
CPU Socket
CPU Cores
MEMORY CONTROLLER
RAM
1
LLC
Packet
RXd
NIC
UPI CONTROLLER
Any QPI traffic will inevitably hurt performance.
If unavoidable, watch for link utilization

## Slide 15: Intel® Vtune Amplifier

## Slide 16: Intel® Vtune Amplifier
1
PCIe bandwidth with traffic breakdown per physical device
https://software.intel.com/en-us/intel-vtune-amplifier-xe
Intel DDIO misses resulted in write back to RAM
MMIO traffic. Avoid Reads and control Writes
DRAM bandwidth
Socket interconnect traffic

## Slide 17: Performance Counter Monitor (PCM)
https://github.com/opcm/pcm

## Slide 18: DPDK ip_pipeline Forwarding Example
Intel® Xeon® Platinum 8180
Intel® X710-DA4
10G
10G
10G
10G
Intel® X710-DA4
10G
10G
10G
10G
Intel® X710-DA4
10G
10G
10G
10G
IIO Stack 0
Gen3x8
IIO Stack 1
Gen3x8
IIO Stack 2
Gen3x8
Measure individual PCIe device bandwidth at x4 granularity
Enumerate downstream devices behind each IIO Stack
Monitor both inbound/outbound at DWord granularity
Can monitor VT-d IOTLB miss rate (opCode.txt)
PCIe to system
CPU to PCIe
Notes: The output of the pcm-iio.x showed three different I/O bandwidth coming from 3 different PCIe NIC cards.
First 4x10G receive and transmit 10% of line rate @ 64 bytes.
Second 4x10G receive and transmit 20% of line rate @ 64 bytes.
Third 4x10G receive and transmit 30% of line rate @ 64 bytes.

## Slide 19: Analyzing performance with Intel tools
1
Easy
Advance
Calibrate I/O bandwidth with expected performance
Check for unexpected cross-NUMA traffic
Check for unexpected PCIe MMIO traffic
Optimize workload to make use of Intel DDIO efficiently

## Slide 20: Questions?
Patrick Lu
patrick.lu@intel.com
Roman Sudarikov
roman.sudarikov@intel.com

## Slide 21: Backup

## Slide 22: IIO transaction flow
Inbound Write Flows:
  I2M – get line ownership for IIO, data is not required to be in the LLC
  RFO – get line ownership and data in the LLC/eDRAM for IIO, deliver a copy of the data to IIO
  WbMtoI – IIO delivers data to Cbo, releases ownership
  CLFlush – IIO delivers data to Cbo, flushes to DRAM
Inbound Read and Snoop Flows:
  RdCurrent – LLC delivers data to IIO
  SnpInv – IIO releases ownership always
Peer to Peer Flows:
  NcP2PB – Peer Write or Completion
  NcP2PS – Peer to Peer Read
https://software.intel.com/en-us/blogs/2014/07/11/documentation-for-uncore-performance-monitoring-units

## Slide 23: Configuring IIO transaction flow
Option 1: global per platform
Option 2: per root port
Option 3: per pci transaction